## Slide 1
Copyright © 2019 University of Colorado
[Instructor Name(s)]
[Department Name]
[Video Title]
FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 2
Copyright © 2019 University of Colorado
Establish motivation for learning VHDL
Introduction to VHDL coding
Reinforce key concepts
Objectives

## Slide 3
Copyright © 2019 University of Colorado
Earn a great income writing VHDL for FPGA and ASIC devices
VHDL is more structured than Verilog and faster than schematic capture!
Learn a new language for efficient and reusable problem solving
Why Learn VHDL?

## Slide 4
Copyright © 2019 University of Colorado
[Video Title]
Describing a hardware circuit that will synthesize into FPGA logic cells or gates
Logic is concurrent, not sequential
  FPGA gates are hardware; executes in parallel
  CPU code is software; executes serially
HDL Key Concepts
References: https://en.wikipedia.org/wiki/Field-programmable_gate_array

## Slide 5
Copyright © 2019 University of Colorado
Finite State Machine Example
State encoding
  S(Q1, Q0) = “00”, “10”
State table
INPUT : Reset, Run, Clk
OUTPUT : R Result
STATE : Current, Next
S0
---
R=0
S1
---
R=1
Reset
Run
Run
Reset
Run
Run
Current State |  | IN | Next State |  | OUT
Q1 | Q0 | Run | D1 | D0 | R
0 | 0 | 0 1 | 0 0 | 1 1 | 0 0
0 | 1 | 0 1 | 0 1 | 1 0 | 0 1
1 | 0 | 0 1 | 1 0 | 0 1 | 1 0
1 | 1 | 0 1 | 0 0 | 1 1 | 0 0

## Slide 6
Copyright © 2019 University of Colorado
Finite State Machine Example
Current State |  | IN | Next State |  | OUT
Q1 | Q0 | Run | D1 | D0 | R
0 | 0 | 0 1 | 0 0 | 1 1 | 0 0
0 | 1 | 0 1 | 0 1 | 1 0 | 0 1
1 | 0 | 0 1 | 1 0 | 0 1 | 1 0
1 | 1 | 0 1 | 0 0 | 1 1 | 0 0

## Slide 7
Copyright © 2019 University of Colorado
Finite State Machine Example
S0
---
R=0
S1
---
R=1
Reset
Run
Run
Reset
Run
Run
VHDL Description

## Slide 8
Copyright © 2019 University of Colorado
[Video Title]
VHDL describes hardware implementations
A VHDL design consists of
  Entity : interface = input, output ports
  Architecture : implementation = design logic
Example: AND gate
Introduction to VHDL

## Slide 9
Copyright © 2019 University of Colorado
[Video Title]
Introduction to VHDL
-- (VHDL comment)
-- Import std_logic library
library IEEE;
use IEEE.std_logic_1164.all;
-- Entity
entity ANDGATE is
port ( A : in std_logic;
B : in std_logic;
Y : out std_logic);
end entity ANDGATE;
-- Architecture
architecture RTL of ANDGATE is
begin
Y <= A AND B;
end architecture RTL;

## Slide 10
Copyright © 2019 University of Colorado
[Video Title]
Example: Basic Logic
Introduction to VHDL
Y
E
C
A
B
D

## Slide 11
Copyright © 2019 University of Colorado
Introduction to VHDL
-- (VHDL comment)
-- Import std_logic library
library IEEE;
use IEEE.std_logic_1164.all;
-- Entity
entity BasicLogic is
port (
A : in std_logic;
B : in std_logic;
C : in std_logic;
Y : out std_logic);
end entity BasicLogic;
-- Architecture
architecture RTL of BasicLogic is
Signal D, E : std_logic;begin
D <= NOT C;
E <= A OR B;
Y <= D AND E;
end architecture RTL;

## Slide 12
Copyright © 2019 University of Colorado
VHDL is a structured language
  Entity and Architecture pairs
Gates synthesized into hardware operate concurrently and in parallel
Summary