## Slide 1
Copyright © 2019 University of Colorado
[Instructor Name(s)]
[Department Name]
[Video Title]
FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 2
Copyright © 2019 University of Colorado
Acquire proficiency designing digital circuits with Field Programmable Gate Arrays (FPGA)s
Employ industry-standard tools to design and implement programmable logic solutions using several Hardware Description Language (HDL) design entry methods, including VHDL, Verilog and System Verilog
Build proficiency by designing basic digital programmable logic circuits in VHDL, Verilog and System Verilog
Objectives

## Slide 3
Copyright © 2019 University of Colorado
Recap: FPGA Design Flow
Design Entry: Schematic or HDL
Functional Simulation
Synthesis or Mapping
Place and Route or Fitting
Timing Analysis and Simulation
Programming the Device
Test and Integration
Release

## Slide 4
Copyright © 2019 University of Colorado
FPGA Design Flow: Design Entry
Design Entry: Schematic or HDL
Functional Simulation
Synthesis or Mapping
Place and Route or Fitting
Timing Analysis and Simulation
Programming the Device
Test and Integration
Release

## Slide 5
Copyright © 2019 University of Colorado
FPGA Design Entry Methodologies
Logical correlation between schematic design entry and circuit implementation
Not always transferrable between different FPGA tools and technologies
Difficult to scale for larger designs
Schematic Entry

## Slide 6
Copyright © 2019 University of Colorado
FPGA Design Entry Methodologies
Hardware Description Languages (HDLs)
  VHDL
  Verilog
  System Verilog

## Slide 7
Copyright © 2019 University of Colorado
HDL Key Concepts
Describing a hardware circuit implementation that your tool chain will eventually interpret and synthesize into FPGA logic cells
HDL is concurrent, not sequential
FPGA logic cells are hardware; inherently executes in parallel
CPU code is software; inherently executes in sequence

## Slide 8
Copyright © 2019 University of Colorado
Review the FPGA design flow
Explore FPGA design entry options
Introduce key concepts of using Hardware Description Languages (HDLs) to describe circuit implementations
Summary