## Slide 1
Copyright © 2019 University of Colorado
[Instructor Name(s)]
[Department Name]
[Video Title]
FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 2
Copyright © 2019 University of Colorado
VHDL Assignments : signals and variables
Operators : add, multiply, and everybody shift to the left
Objectives

## Slide 3
Copyright © 2019 University of Colorado
  Signals
    Signal wire to the entity : std_logic
    Scheduled update
    <= signal assignment operator
    Z <= A and B; -- concurrent, gates silicon
    Z <= D after 5ns; -- sequential, simulation
  Variables
    Variable only within the process : integer
    Immediate update
    := variable assignment operator
    count := count +1; --simulation loop counter
    a := 27; -- variable assignment
VHDL Assignments

## Slide 4
Copyright © 2019 University of Colorado
entity mux_4 is port(
a, b, c, d: in std_logic_vector(3 downto 0);
s: in std_logic_vector(1 downto 0);
x: out std_logic_vector(3 downto 0));
end mux_4;
architecture sel_arch of mux_4 is
begin
with s select
x <= a when “00”;
b when “01”;
c when “10”;
d when “11”;
d when others;
end sel_arch;
Select Assignment
References: Kevin Skahill, VHDL for Programmable Logic.
Menlo Park, CA, Addison-Wesley, 1996, pp. 166

## Slide 5
Copyright © 2019 University of Colorado
architecture sel_arch of mux_4 is
begin
x <= a when ( s =“00”) else
b when ( s =“01”) else
c when ( s =“10”) else
d;
end sel_arch;
Conditional Assignment
References: Kevin Skahill, VHDL for Programmable Logic.
Menlo Park, CA, Addison-Wesley, 1996, pp. 166

## Slide 6
Copyright © 2019 University of Colorado
architecture sel_arch of mux_4 is
begin
mux_proc: process(a, b, c, d, s)
begin
if s = “00” then x <= a;
elsif s = “01” then x <= b;
elsif s = “10” then x <= c;
else x <= d;
end if;
end process mux_proc;
end sel_arch;
Process Assignment
References: Kevin Skahill, VHDL for Programmable Logic.
Menlo Park, CA, Addison-Wesley, 1996, pp. 166

## Slide 7
Copyright © 2019 University of Colorado
[Video Title]
Operators
  ** exponent abs absolute value
  not complement + - add or subtract
  * multiply / divide
  mod modulo rem remainder
  sll, srl shift left, right
  rol, ror rotate left, right
  =, /=, <, <=, >, >= equality, greater, less than
  and, or, nand, nor, xor, xnor
Order precedence
  Left to right, Parenthesis
  Unary single operand on right mod A
  Binary operators on both sides A+B
VHDL Operators

## Slide 8
Copyright © 2019 University of Colorado
Array
  string “abc”
  bit_vector “1001”
  std_logic_vector “101Z”
Scalar
  character ‘a’
  bit ‘1’, ‘0’
  std_logic ‘1’, ‘0’, ‘X’, ‘Z’
  boolean true, false
  real, integer 3.14 1E+0, 27
  time fs, ps, ns, us, ms
Data Types – scalar and array types

## Slide 9
Copyright © 2019 University of Colorado
VHDL Assignments : signal and variable
  Logical Select
Operators - Dial 0
Scalar and Array data types
Summary