## Slide 1
Copyright © 2019 University of Colorado
[Instructor Name(s)]
[Department Name]
[Video Title]
FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 2
Copyright © 2019 University of Colorado
VHDL rules and syntax
Understand VHDL Constructs
Objectives

## Slide 3
Copyright © 2019 University of Colorado
Case Sensitivity
  VHDL is not case sensitive. Equivalent :
    DATA_out <= A_in and B_in;
    data_OUT <= a_IN AND b_IN;
Tabs and Spaces
  Use for readable coding style. Equivalent :
    D_out <= a_in or b_in;
    D_out <= a_in or b_in;
Comments
  -- dash dash at the beginning or end of line
Semicolon ; Terminates each statement
VHDL Rules and Syntax

## Slide 4
Copyright © 2019 University of Colorado
Deconstructing VHDL Components
-- Use standard IEEE library
library IEEE;
use IEEE.std_logic_1164.all;
-- Entity
entity Comparator is port (
A,B : in std_logic_vector(3 downto 0);
Result : out std_logic);
end Comparator;
-- Architecture
-- Dataflow description
architecture dataflow of Comparator is
begin
Result <= '1' when (A=B) else '0';
end dataflow;

## Slide 5
Copyright © 2019 University of Colorado
Library : IEEE Standard
-- Use standard IEEE library
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all; -- arithmetic
Library is text readable (take a look inside)
  Defines standard types : std_ulogic
  1 logic one, strong drive
  0 logic zero, strong drive
  X unknown value, strong drive
  Z high impedance, tri-state . . .
Defines Functions : and
-- truth table for "and" function
CONSTANT and_table : stdlogic_table := (
-- ----------------------------------------------------
-- | U X 0 1 Z W L H - | |
-- ----------------------------------------------------
( 'U', 'U', '0', 'U', 'U', 'U', '0', 'U', 'U' ), -- | U |
( 'U', 'X', '0', 'X', 'X', 'X', '0', 'X', 'X' ), -- | X |
( '0', '0', '0', '0', '0', '0', '0', '0', '0' ), -- | 0 |
( 'U', 'X', '0', '1', 'X', 'X', '0', '1', 'X' ), -- | 1 | . . .

## Slide 6
Copyright © 2019 University of Colorado
Entity : Interface ports
-- Entity
entity Comparator is port (
A,B : in std_logic_vector(3 downto 0);
Result : out std_logic);
end Comparator;
Ports : blackbox
  Direction
  in input
  out output
  inout bi-directional
    Vector (bus, bundle) and bit
  std_logic_vector (3 downto 0) bus 1,0,X,Z,W,L,H,U,-
  std_logic bit 1,0,X,Z,W,L,H,U,-
  unsigned (127 downto 0) bus (full 128 bits data)

## Slide 7
Copyright © 2019 University of Colorado
Architecture : Design
-- Architecture
architecture dataflow of Comparator is
begin
Result <= '1' when (A=B) else '0';
end dataflow;
Functional definition of circuit design
  Simple to Complex
  Code re-usable
  Chip top to lowest hierarchy
  Instantiate
  architecture MY_HIER of MY_UPPER is
  component MY_LOWER_OR port (A,B: in std_logic; Z: out std_logic);
  end component;
  begin
  MY_INST_1: MY_LOWER_OR port_map (A=>A_UP, B=>B_UP, Z=>Z_UP);
  end architecture MY_HIER;

## Slide 8
Copyright © 2019 University of Colorado
Create readable code style by using :
  Spaces, tabs
  Other readable code sources as examples
  Use comments before and on each line
Library, Entity, Architecture
Summary